USING hp3478ext AS UNIVERAL USB-UART-GPIB ADAPTER

GPIB DEBUGGER

hp3478ext implements basic line editor and command history. While entering GPIB commands interactively doesn't seem to be practical for everyday use, it's quite useful for checking individual commands and learning how particular device behaves.
Line editor keys:
ENTER (\r) execute command
UP (\x27[A) previous command in history list
DOWN (\x27[B) next command in history list
LEFT (\x27[D) move cursor left
RIGHT (\x27[C) move cursor right
BACKSPACE (\b),
DELETE (\x7f) delete character before the cursor
When used from software, interactive mode should be turned off with O1 or OI0 commands.

COMMAND REFERENCE

D: transmit or receive ASCII data (ATN off)
Command receives data if the adapter is in LISTEN state. End of transmission is determined by receive end sequence (OR command). Absence of data (timeout) is presented with an empty string.
Command transmits data if the adapter is not in LISTEN state. Payload immediately follows the command character. Depending on the OT (transmit end sequence) setting, transfer is terminated with EOI, \r or \n.
Response:
    OK\r\n transmission complete
    TIMEOUT <len>\r\n time out waiting for device while transmitting
        <len> is number of bytes actually transmitted
    \r\n time out waiting for device while receiving
    <payload> data received from the device

C: transmit ASCII command (ATN on)
Command transmits ASCII bytes with ATN signal turned on. Transferred data is analysed to set the bus state as follows:
- GPIB adapter will enter LISTEN state if it's listen address (+32) is in the command string.
- GPIB adapter will exit LISTEN state if it's talk address (+64) or unlisten command (?) is in the string.
Response:
    OK\r\n transfer complete
    TIMEOUT <len>\r\n time out waiting for device
        <len> is number of bytes actually transmitted

R, L: control REN signal
R turns REN on, L turns REN off.
Response:
OK\r\n

I: clear interface
Turns IFC signal on for 1ms. GPIB adapter will exit LISTEN state.
Response:
OK\r\n

S: get status
Returns state of SRQ and REN lines as two ASCII characters 0 or 1. The third character is the GPIB adapter state: 0 = TALK, 1 = LISTEN. In contrast to LISTEN, in TALK state it actually doesn't verify whether its TALK address was sent or not.
Response:
000\r\n	three characters, see above

P: enter "plotter" mode
In plotter mode GPIB adapter continuously attempts to read data from the bus. Send ESCAPE (\x27) to exit plotter mode.
Response:
    <data>

O: option setting
O<opt><val> set option <opt> to decimal <val>
O<opt> request option value
O? list available options
O<opt><val>w set option <opt> to <val> and remember it in EEPROM
O0 set defaults for interactive operation
O1 set defaults for non interactive operation

Available options (<opt>):
X 1 = enable HP3487A extension mode, this mode conflicts with GPIB commands
     described in this document.
     0 = GPIB adapter mode, disables HP3487A extension.
R Receive end sequence specifies when THD, TUD and D commands would stop.
     1 = CR, 2 = LF, 4 = EOI Those bits may be ORed together, then on any of
     specified conditions will stop the transfer.
T Transmit end sequence specifies what to send after the data supplied
     with D command. It accepts the same values as R option. For example,
     7 means to send CR followed by LF with EOI.
I 0 = disable interactive mode. Turns off line editor and echoing of commands,
     disables <GPIB> prompt.
     1 = enable interactive mode.
C Controller GPIB address. This address is recognised in GPIB commands so
     the adapter knows it's in LISTEN state.
D Device GPIB address. The address of HP3478A, this is only used in HP3478
     extension mode. But if this address is set to 31, the adapter will enter
     “plotter” mode upon start up (as if P command was entered).
B Baud rate. 0 = 115200, 2 = 500K, 3 = 1M, 4 = 2M. Note that it depends
     on the USB-UART chip used, whether the setting would work.

Response:
<opt_help>	text for O?
<val>\r\n	option value in decimal
OK	option is set
ERROR\r\n	incorrect command syntax or value
WRONG OPTION\r\n	unknown option

?: quick help
Prints command summary.

H: command list
Prints command history.

T: binary and hex transfer commands
THC transmit hex command
TBD transmit binary data
TBD<len> receive binary data
THD transmit hex data
THD<len> receive hex data

Data transmit or receive operation is determined by the LISTEN state of the adapter. I.e. T is interpreted as receive, if adapter is addressed as listener. THC always transmits. <len> is optional. It is one byte hex value and specifies maximum number of characters to receive.
HEX data is an arbitrary length hex string terminated with an optional ; and \r\n The line is terminated with EOI by default , so ; means that there is no EOI. When transmitting, whole command buffer is limited by 64 bytes. The maximum payload size is (64 - sizeof("THD") - sizeof("\r")) = 30 bytes. There's no limit on the received hex string length.
Binary data consists of blocks prefixed with one-byte length. Block length is up to 127 bytes. High order bit of length byte represents EOI at the end of the block. Transfer is terminated with 0 byte (i.e. length = 0).
Response:
   ERROR\r\n wrong command syntax
   TIMEOUT <len>\r\n time out while transmitting
        (<len> = number of bytes sent in decimal)
   OK\r\n send complete for TH commands
   ;\r\n time out receiving data for THD command
   <payload> binary or hex payload (see below)
   <txlen> status byte = number of bytes transmitted for each block (see example below)

EXAMPLES

In all examples below "=> " stands for request, "<= " stands for response. \-escaped characters are non-printable characters in C notation. If the example demonstrates use of interactive mode, dialogue is presented as it is seen on the terminal, no special characters are shown.

Example 1: data formats
Following example explains how to send EOI-terminated "HELLO WORLD\n" string in various formats.

Hex transmission:
=> THD48454c4c4f20;\r
<= OK\r\n
=> THD574f524c44210a\r
<= OK\r\n

Binary transmission:
=> TBD\r\x06HELLO \x87WORLD!\n
<= \x06\x07

ASCII transmission:
=> OT6\r\n
<= OK\r\n
=> DHELLO WORLD!
<= OK\r\n

Example 2: getting reading from HP3478A
Following assumes default controller address 21 and multimeter address 23.

<GPIB> CW5
OK
<GPIB> D
+1.87978E+0
<GPIB>

Example 3: serial poll - reading status byte
<GPIB> THC183557
OK
<GPIB> THD1
01;
<GPIB> THC19